COMPRESSED AIR SYSTEMS, INC.

9303 Stannum Street

Tampa FL 33619-2658

“Where Sales and Service Go Hand in Hand.”

Phone  813-626-8177        FAX: 813-628-0187	   Toll Free 800-881-1942

www.compressedairsystems.com

POGO I, II, III

Operation Manual

Always operate, inspect and maintain this tool with American National Standards Institute Safety Code for Portable Air Tools (ANSI B186.0) and any other applicable safety codes and regulations.

WARNING

Always turn off the air supply and disconnect the air supply hose before installing, removing or adjusting any accessories on the tool or before performing any maintenance on this tool.  Failure to do so could result in injury.

Never use higher air pressure to increase the output of the gate opener.  Overloading will drastically shorten the life of all internal parts.

IMPORTANT

Make sure that these instructions are fully understood before operating this tool.  The tool, its attachments and accessories must only be used for their designed purpose.  For product liability and safety reasons, any modifications of the tool and its accessories must be agreed upon by the technical authority of the manufacturer.  All locally legislated safety rules with regard to installation, operation and maintenance shall be respected at all times.

INSTRUCTIONS FOR SAFE OPERATION

1.	First, follow your local safety regulations.

2.	Always wear safety goggles and gloves.

3.	Keep hands, loose clothing and long hair away from rotating end of the tool.

4.	Anticipate and be alert for sudden changes in motion during start up and operation of any power tool.

5.	The tool shaft may continue to rotate briefly after the throttle is released.

6.	Do not lubricate the tool with flammable or volatile liquids such as kerosene, diesel or jet fuel.

7.	Use only step tapered adapter bits which have been heat treated and are designed for impacting type openers (part #203-001).

8.	Always check for damaged or loose hoses and fittings before operation, and replace if necessary.  Whipping hoses can cause serious injury.  Always use safety clips on all air hose connections.

9.	Keep body working stance balanced and firm.

10.	Always wear hearing protection when operating this tool.

11.	When moving tool from one location to another, do not run over uncovered surfaces and move slowly and deliberately.

AIR SUPPLY

Air Hose Size:	Use a 1" ID hose to insure adequate air supply.

Air Pressure:	85 PSI (6 kb/cm2) air pressure is recommended for the most efficient performance.  Too high of air pressure will shorten the life of the tool.

Air Quality:	It is important that the compressed air supplied to the opener is clean and dry.  A properly sized dryer and filters are recommended.

LUBRICATION

For Air Motor:	A good quality air tool oil should be kept in the lubricator at all times.  Recommended lubricant is 10 W/NR Non Fluid Oil *.  (see attached spec sheet)

For Bearings:	Supply high quality grease when the tool is overhauled.  Recommended grease HD-927/MS (see attached spec sheet).

*WARNING:	When adding oil to the lubricator, the air supply should be shut off and the remaining air pressure left in the machine should be bled off by depressing the throttle lever until the tool stops.  If the lubricator is supplied with a pressure bleed type filler cap, depress the red button to insure all air pressure has been vented to atmosphere.

MAINTENANCE

Regular Overhaul:	Periodical overhaul by a competent repair technician to assure the best performance, trouble free operation and maximum tool life.

TO OPEN GATES

The operator should position the Pogo perpendicular to the railcar.  Advance the Pogo forward until the Hex-3 bit is fully engaged into the capstan. Once the bit is fully engaged into the capstan flip the lever that controls the turning of the wheels (POGO III Model only).  When the wheels are turned parallel to the track the throttle lever can be depressed to open or close the gates (see the next paragraph for tips for proper technique) On Models I & II once the bit is fully engaged maintain slight forward pressure while depressing the throttle lever.

NOTE: Failure to keep the Hex-3 bit fully engaged will result in unnecessary wear to the bit.

FOR EASY TO OPEN GATES

The throttle should be depressed in short rapid spurts lasting only a second or two.  Each time the throttle is depressed, the gate will move a little.  Do this until the gate is in the desired position.

Operating the Pogo in this manner will prevent the gate from slamming hard into the stops which could cause damage to the gate.

FOR MORE DIFFICULT GATES

The throttle should be depressed completely until the gate moves approximately 1/3 of the way.  Once the gate has broken loose and opened partially, the standard techniques used for easy to open gates can then be used.

IMPORTANT NOTICE: After each use depressurize the lubricator by pushing the red button on the filler cap.  Failure to do this will cause the oil to continue to flow to the tool even while not in use, resulting in unnecessary waste of the air tool oil.

WARNING !!

Hammering on a gate after it has been opened for the purpose of facilitating material flow should not be allowed.  The Pogo is not a vibrator and should not be used as such.

This device was developed to make the job of opening gates safe and easy.  When operated properly the Pogo will provide years of trouble free service.