COMPRESSED AIR SYSTEMS, INC.

9303 Stannum Street

Tampa FL 33619-2658

“Where Sales and Service Go Hand in Hand.”

Phone  813-626-8177        FAX: 813-628-0187	   Toll Free 800-881-1942

www.compressedairsystems.com

POGO IV

Operation Manual

Always operate, inspect and maintain this tool with American National Standards Institute Safety Code for Portable Air Tools (ANSI B186.0) and any other applicable safety codes and regulations.

WARNING

Always turn off the air supply and disconnect the air supply hose before installing, removing or adjusting any accessories on the tool or before performing any maintenance on this tool.  Failure to do so could result in injury.

Never use higher air pressure to increase the output of the gate opener.  Overloading will drastically shorten the life of all internal parts.

IMPORTANT

Make sure that these instructions are fully understood before operating this tool.  The tool, its attachments and accessories must only be used for their designed purpose.  For product liability and safety reasons, any modifications of the tool and its accessories must be agreed upon by the technical authority of the manufacturer.  All locally legislated safety rules with regard to installation, operation and maintenance shall be respected at all times.

INSTRUCTIONS FOR SAFE OPERATION

1.	First, follow your local safety regulations.

2.	Always wear safety goggles and gloves.

3.	Keep hands, loose clothing and long hair away from rotating end of the tool.

4.	The Pogo IV should be operated with the operator standing at the end of the package with the control levers and steering arm.

5.	Never reach into the Pogo IV frame with feet or hands without first disconnecting and bleeding off the air supply!

6.	Never operate the up/down, in/out controls while others are working on or near the Pogo IV.

7.	Anticipate and be alert for sudden changes in motion during start up and operation of any power tool.

8.	The tool shaft may continue to rotate briefly after the throttle is released.

9.	Do not lubricate the tool with flammable or volatile liquids such as kerosene, diesel or jet fuel.

10.	Use only step tapered adapter bits (part #203-001) which have been heat treated and designed for impacting type openers.

11.	Always check for damaged or loose hoses and fittings before operation, and replace if necessary.  Whipping hoses can cause serious injury.  Always use safety clips on all air hose connections.

12.	Keep body working stance balanced and firm.

13.	Always wear hearing protection when operating this tool.

14.	When moving tool from one location to another, do not run over uncovered surfaces and move slowly and deliberately.

Page 1 of 3

POGO IV

Operation Manual

LUBRICATION

For Air Motor:	   A 10W quality air tool oil should be kept in the lubricator at all times. Recommended lubricant is 10 W/NR Non Fluid Oil *.

For Bearings:	Supply high quality grease when the tool is overhauled.  Recommended grease HD-927/MS.

*WARNING:	When adding oil to the lubricator, the air supply should be shut off and the remaining air pressure left in the machine should be bled off by depressing the throttle lever until the tool stops.  If the lubricator is supplied with a pressure bleed type filler cap, depress the red button to insure all air pressure has been vented to atmosphere.

MAINTENANCE

Regular Overhaul:		Periodical overhaul by a competent repair technician to assure the best performance, trouble free operation and maximum tool life.

CONNECTION TO AIR SUPPLY

Air Hose Size:	Use a 1" ID hose to insure adequate air supply. Always use safety clips on all air hose connections.

Air Pressure:	90 to 110 PSI air pressure is recommended for the most efficient performance.  Too high of air pressure will shorten the life of the machine.

Air Quality:	It is important that the compressed air supplied to the opener is clean and dry.  A properly sized dryer and filters are recommended.

Adjusting the in / out

cylinder air cushion

regulator:			Upon initial connection of the machine to the air supply the mini regulator mounted between the lubricator

and the throttle valve should be set at approximately 15 to 20 pounds lower than the line pressure. This

should be done first before operating any of the control levers. The function of this regulator is for the

purpose of applying an air cushion to the front side of the in / out cylinder during initial pressurization of

the machine. This prevents the drive mechanism from jumping forward in an abrupt manor when the

in / out control lever is activated for the first time after the initial pressurization of the machine. This

regulator also supplies air pressure to the forward / reverse lever control valve.

HOW TO USE

Step One:	Using the steering arm lever, align the Pogo IV so the wheels and frame are parallel to the tracks.  The Hex-3 drive bit should be 8" or less away from the face of the capstan.

Note: The power unit should be fully retracted back into the frame while positioning the Pogo IV.

Step Two:	Raise the power unit until the Hex-3 bit is in-line with the capstan.

Page 2 of 3

POGO IV

Operation Manual

HOW TO USE CONTINUED

Step Three:	Advance the power unit forward engaging the Hex-3 bit into the capstan.  At this time, make sure the Hex-3 bit and the power unit are horizontal and in-line with the capstan shaft.  If necessary, raise or lower the power unit for proper alignment.  Once again advance the power unit until the Hex-3 bit is fully engaged with the capstan.

Step Four:	Check the power drive forward/reverse lever position; place the lever in the direction you want the drive to turn.

Step Five:	You are now ready to open or close the slide gate.  For easy to open gates, the throttle should be depressed in short rapid spurts lasting only a second or two.  Each time the throttle is depressed, the gate will move a little.  Do this until the gate is in the desired position. Operating the Pogo in this manner will prevent the gate from slamming hard into the stops which could cause damage to the gate. For more difficult to open gates, the throttle should be depressed completely until the gate moves approximately 1/3 of the distance.  Once the gate has broken loose and opened partially, the standard technique used for easy to open gates can then be used.

IMPORTANT NOTICE: After each use depressurize the lubricator by pushing the red button on the filler cap.  Failure to do this will cause the oil to continue to flow to the tool even while not in use, resulting in unnecessary waste of the air tool oil.

WARNING !!!!!!!!

Hammering on a gate after it has been opened for the purpose of facilitating material flow should not be allowed.  The Pogo is not a vibrator and should not be used as such.

This device was developed to make the job of opening gates safe and easy.  When operated properly the Pogo will provide years of trouble free service.

HOW TO DISENGAGE

Retract the power drive unit.  Sometimes the bit will become wedged tight into the capstan.  If this occurs, raise and lower the power drive unit slightly.  If the bit still remains stuck, then move the power drive forward/ reverse lever to the opposite direction and slightly bump the throttle lever.  This will cause the bit to release.  Continue to retract the power drive unit completely into the frame.

Using the steering arm lever, it is now possible to swing the Pogo IV out and away from the car.

Page 3 of 3